## Slide 1
Target Network
Out-Side
Router/Switch
ISP Internal Network
In-Side
Switch
External Link, both TX and RX
Internal Link, both TX and RX
Firewall
Example of network interconnection before NIA Installation on classical network (single link)

## Slide 2
Target Network
Out-Side
Router/Switch
ISP Internal Network
In-Side
Switch
Firewall
Example of NIA installation with SPAN Port in a classical network (single link)
NIA Monitoring Network Interface
The only difference between Ethernet and Fiber interconnection is related to GBIC to use on NIA DAG Card
The Injection wil be performed through the
main NIA network interface (ethernet)
2
3
External Link, both TX and RX
Internal Link, both TX and RX
SPAN/Mirror Port, both TX and RX
1
According to DSLAM position the NIA could be connected both to Internal or External side of network

## Slide 3
Ethernet Network Tap
NIA Monitoring Network Interface
2
3
Target Network
ISP Internal Network
Out-Side
Router/Switch
(access or distribution)
The network signal is duplicated so the monitoring device has full access to the signal.
The monitoring device sees the same traffic as if it were also in-line, including physical layer errors.
External Link, both TX and RX
Internal Link, both TX and RX
Replicated TX from Internal Link
Replicated TX from External Link
Firewall
4
In-Side
Switch (core)
Example of NIA installation with Ethernet TAP usage in a classical network (Ethernet single link)
1
The passive Tap provides a permanent in-line access port to monitor all full-duplex traffic without data stream interface.
The Injection wil be performed through the main NIA network interface (ethernet)

## Slide 4
Fiber Network Tap
NIA Monitoring Network Interface
2
1
3
Target Network
ISP Internal Network
Out-Side
Router/Switch
(access or distribution)
The network signal is split so the monitoring device has full access to the signal.
The monitoring device sees the same traffic as if it were also in-line, including physical layer errors.
The passive Tap provides a permanent in-line access port to monitor all full-duplex traffic without data stream interface.
External Link, both TX and RX
Internal Link, both TX and RX
Replicated TX from Internal Link
Replicated TX from External Link
Firewall
The Injection wil be performed through the main NIA network interface (ethernet)
4
Example of NIA installation with Fiber TAP usage in a classical network (single link)
In-Side
Switch (core)

## Slide 5
Primary Link to Access Network, could be configured both Active/Passive or Active/Standby
Secondary Link to Access Network, could be configured both Active/Passive or Active/Standby
Example of network interconnection before NIA Installation in a redundant network (double link)
Target Network
Secondary ISP Network Branch
Primary
Router/Switch
Secondary
Router/Switch
Primary
Firewall
Primary ISP Network Branch
Secondary
Firewall

## Slide 6
NIA Monitoring Network Interface
2
The monitoring device sees the traffic aggregated by the DAG Card.
SPAN/Mirror Port on Primary Link, both TX and RX
SPAN/Mirror Port on Secondary Link, both TX and RX
4
Example of NIA installation in a redundant network (double link)
The NIA must be directly connected to both Primary and Secondary branches of the network
1
The only difference between Ethernet and Fiber interconnection is related to GBIC to use on NIA DAG Card
3
Target Network
Secondary ISP Network Branch
Primary
Router/Switch
Secondary
Router/Switch
Primary
Firewall
Primary ISP Network Branch
Secondary
Firewall
The Injection wil be performed through the main NIA network interface (ethernet)